Location	Address	Contact Name	Contact Phone	Scope Pages
Satellite	187 Bd Accra Etd Rd Lotis La Colline Mohammedia, CP-28810, Morocco, 28810	Mohamed Hafid	+212661081224	1-2

Satellite location

MEASURED QUANTITY or DEVICE TYPE CALIBRATED	RANGE	UNCERTAINTY1,2 (±)	CALIBRATION METHOD OR PROCEDURE, STANDARD EQUIPMENT USED (OPTIONAL)
TESTING
Clean rooms and related controlled environments

Security Post / Microbiological	Number of particles depending on / diameter	≥ ISO 5 / ≥ Classe A	Measurement using a meter / particle optics
	Downward speed	0,2 m/s à 20 m/s	Measuring with an anemometer / hot wire type
	Volume flow	50 m3/h à 3000 m3/h	Measurement with a wire anemometer / hot
	Differential pressure	de -1000 Pa à 1000 Pa	Measurement with pressure gauge
	Filter integrity	de 0,001 % à 100 %	Generation of an aerosol and measurement of penetration in downstream of the filter with a photometer
Clean rooms and / environments / controlled and / related	Number of particles depending on / diameter	≥ ISO 5 / ≥ Classe A	Measurement using a meter / particle optics
	Recovery time	≤ 30 min	Particle counting at intervals of / regular time after contamination using / from an aerosol
Clean rooms and / environments / controlled and / related	Air speed	0,2 m/s à 20 m/s	Measurement with a hot wire type anemometer / Measuring with a propeller anemometer
	Differential pressure	de -1000 Pa à 1000 Pa	Measuring with a pressure gauge
	Temperature	10 °C à 50 °C	Measuring with a thermometer
	Relative humidity	0% to 80% / (For T included / between -10°C and 50°C)	Measure with a hygrometer
	Air flow	50 m3/h à 4 250 m3/h	Measurement with a hot wire anemometer
	Filter integrity	De 0,001 % à 100 %	Generation of an aerosol and measurement of / penetration downstream of the filter with a / photometer

MEASURED QUANTITY or DEVICE TYPE CALIBRATED	RANGE	UNCERTAINTY1,2 (±)	CALIBRATION METHOD OR PROCEDURE, STANDARD EQUIPMENT USED (OPTIONAL)
Establishments / health - Areas / to environment / mastered	Number of particles depending on / diameter	≥ ISO 5 / ≥ Classe A	Measurement using a meter / particle optics
	Kinetics of / decontamination	≤ 30 min	Particle counting at intervals of / regular time after contamination using / from an aerosol
	Air speed	0,2 m/s à 20m/s	Measurement with a hot wire type anemometer / Measuring with a propeller anemometer
	Differential pressure	de -1000 Pa à 1000 Pa	Measuring with a pressure gauge
	Temperature	10 °C à 50 °C	Measuring with a thermometer
	Relative humidity	0% to 80% / (For T included / between -10°C and 50°C)	Measure with a hygrometer
	Air flow	50 m3/h à 4 250 m3/h	Measurement with a hot wire anemometer
	Filter integrity	De 0,001 % à 100 %	Generation of an aerosol and measurement of / penetration downstream of the filter with a / photometer

Compressed Air
compressed air qualification	Particle counting	≥ class 2	Measurement using a meter / particle optics
	Determination of oil content (aerosols and oil vapors)	≥ class 2	Measurement using fluorescence detectors
	Determination of dew point / humidity level	≥ class 2	Measurement using a dew point
AIR & SURFACE MICROBIOLOGICAL SAMPLING	number of bacteria	≥ Zone classe A (iso5)	Environmental Surface Sampling Using Contact Agar Plates